## Slide 1: Interfacing Android Things with an Arduino Real-World Experience and Observations
Timothy J. Salo
Salo IT Solutions, Inc.
salo <at> saloits <dot> com

## Slide 2: Interfacing Android Things
Android Things “Makes embedded development as simple as mobile development has become”
  - Dave Smith, Google I/O 2017

## Slide 3: Interfacing Android Things
Objectives
Better understand Android Things’ applicability:
  Does Android Things gracefully support typical embedded tasks?
    Directly manipulate hardware devices?
    Handle interrupts and asynchronous events?
  Do Java Threads easily support full-duplex, interrupt-driven devices?

## Slide 4: Interfacing Android Things
Presentation
Presentation and Code
  <https://github.com/tjsalo/>
Presentation
  <https://www.saloits.com/papers/InterfacingAndroidThingsIoTDevfest2018.pdf>

## Slide 5: Interfacing Android Things
Contents
The project
Observations, lessons learned, and opinions

## Slide 6: Interfacing Android Things: The Project
The Project
Interconnect:
  Raspberry Pi running Android Things and Pololu A-Star
Transfer:
  Temperature sensor data from A-Star to RPi
Display:
  Temperature sensor data on web page

## Slide 7: Interfacing Android Things: The Project
Android Things / Arduino Interfacing
Raspberry Pi
A-Star Arduino
Temperature Sensor
Web Browser
Async Cable
I2C Bus
SPI Bus
Temp Values
HTTP

## Slide 8: Interfacing Android Things: The Project
SSID: AndroidThings
http://192.168.0.56:8080

## Slide 9: Interfacing Android Things: Hardware
Raspberry Pi
Quad Core Broadcom BCM2837 64-bit CPU
1 GB RAM
64 GB Flash
1.2 GHz
3.3 V logic
Android Things
NanoHttpd
Pololu A-Star 32U4
Atmel ATmega32U4 8-bit MCU
2.5 KB RAM
32 KB flash
16 MHz clock
5 V logic
No operating system
Custom C code

## Slide 10: Interfacing Android Things: Hardware
Raspberry Pi
Quad Core Broadcom BCM2837 64-bit CPU
1 GB RAM (x 400,000)
64 GB Flash (x 2,000,000)
1.2 GHz (x 75)
3.3 V logic
Android Things
NanoHttpd
Pololu A-Star 32U4
Atmel ATmega32U4 8-bit MCU
2.5 KB RAM
32 KB flash
16 MHz clock
5 V logic
No operating system
Custom C code

## Slide 11: Interfacing Android Things: Hardware
Connecting Raspberry Pi / A-Star Arduino
A-Star has Raspberry Pi Bridge
  40-pin Raspberry Pi GPIO connector
But…
  Raspberry Pi uses 3.3 V logic
  A-Star uses 5 V logic

## Slide 12: Interfacing Android Things: Hardware
Connecting Raspberry Pi / A-Star Arduino
Therefore:
  Level converters required on signal pins
Furthermore:
  Only I2C signals actually connected to 40-pin connector
    with level converters
  Rest of signal pins not connected!

## Slide 13: Interfacing Android Things: Interfaces
Communications interfaces
Async | I2C | SPI
Full-Duplex | Half-Duplex | Full-Duplex
Peer-to-Peer | Master/Slave | Master/Slave
Asynchronous (no clock signal) | Synchronous (clock signal) | Synchronous (clock signal)

## Slide 14: Interfacing Android Things: Interfaces
Async Link
Serial asynchronous link
Two data signals
  Transmit data
  Receive data

## Slide 15: Interfacing Android Things: Interfaces
Async Link
Raspberry Pi
Arduino
Transmit Data
Receive Data
Receive Data
Transmit Data
Note: Ground not shown.

## Slide 16: Interfacing Android Things: Interfaces
I2C Protocol
Inter-integrated Circuit (I2C) Protocol
Two signals:
  Serial data (SDA)
  Serial clock (SCL)

## Slide 17: Interfacing Android Things: Interfaces
I2C Protocol
Raspberry Pi
Arduino
SDA
SDA
SCL
SCL
Note: Ground not shown.
I2C Master
I2C Slave

## Slide 18: Interfacing Android Things: Interfaces
Serial Peripheral Interface (SPI) bus
Serial bus used in embedded systems
Master / Slave operation
Full duplex (sort of – still Master/Slave)
I/O operation swaps value of a register in the Master and the value of a register in the Slave
Can delineate frames

## Slide 19: Interfacing Android Things: Interfaces
Serial Peripheral Interface (SPI) bus
Raspberry Pi
SPI Master
Arduino
SPI Slave
MOSI
MOSI
MISO
MISO
Register
Register
SPI I/O operation swaps Master register and Slave Register values. (Actually, performs a bit-wise end-around-shift.)

## Slide 20: Interfacing Android Things: Interfaces
Serial Peripheral Interface (SPI) bus
Android Things supports two data transfer modes:
  Half-duplex data transfer
  Full-duplex data transfer
Remember: data transfer controlled by Master

## Slide 21: Interfacing Android Things: Interfaces
Serial Peripheral Interface (SPI) bus
Raspberry Pi
SPI Master
Arduino
SPI Slave
MOSI
MOSI
MISO
MISO
SCLK
SCLK
~SS
~SS
Note: Ground not shown.

## Slide 22: Interfacing Android Things: Interfaces
Serial Peripheral Interface (SPI) bus
Raspberry Pi
SPI Master
Arduino
SPI Slave
MOSI
MOSI
MISO
MISO
SCLK
SCLK
~SS
~SS
Level Shifter
Level Shifter
Level Shifter
Level Shifter
Note: Soldering probably required

## Slide 23: Interfacing Android Things: Communications
Communications “Protocol”
Messages are ASCII strings, terminated by /n
Master
Slave
hello: nnnnn
ack: nnnnn
send: temp
temp: nn.n

## Slide 24: Interfacing Android Things: Communications
Idle
Timeout
Hello Sent
Tx: hello <seq>
Link Established
Rx: ack <seq>
Timeout
Send Sent
Tx: send temp
Rx: temp <value>

## Slide 25: Interfacing Android Things: Software
Typical Embedded Software Architecture
Update clock (e.g., millisecond clock)
While (true):
  Executing pending tasks
  Process expired timers (execute tasks)
Handle interrupts
  Manage peripherals / communications / clock/ …

## Slide 26: Interfacing Android Things: Software
Planned Android Things Software Architecture
Main Thread:
  Android stuff
  Fire up other threads
  Create web pages
  A bit of coordination
One Thread per physical interface
  Manage link, communications

## Slide 27: Interfacing Android Things: Project Results
Project Results
Implementation results decidedly mixed
Some stuff worked, some stuff didn’t
  Async Interface works well
  I2C interface largely works
    RPi hardware bug (I2C clock stretching)?
  SPI interface barely works
    Noisy connections to level shifters?

## Slide 28: Interfacing Android Things: Observations
Observations
Android Things ecosystem
What is “embedded programming”?
Java Thread and asynchronous events
Java String
Hardware state visibility
Low-level development
Mobile developers don’t…
Whither Android Things?

## Slide 29: Interfacing Android Things: Observations
Caveats
I am not an Android developer
I am not a Java programmer
I am not an electrical engineer
Long ago, I was an assembly language systems programmer

## Slide 30: Interfacing Android Things: Observations
Android Things Ecosystem
The Android Things ecosystem has many nice capabilities
    Android Studio
      Leverage Android developer expertise / documentation / …
      Leverage Android code base / examples / …
      Rich IDE
      adb
      …

## Slide 31: Interfacing Android Things: Observations
Android Things Ecosystem
The Android Things ecosystem has many nice capabilities
    Over-the-air (OTA) software updates
      Addresses one of the more vexing IoT problems

## Slide 32: Interfacing Android Things: Observations
Android Things Ecosystem
The Android Things ecosystem has many nice capabilities
    Android Things Console
      Has potential
      Feels like a prototype

## Slide 33: Interfacing Android Things: Observations
Android Things Ecosystem
The Android Things ecosystem has many nice capabilities
    User-level device drivers
      Capability has potential
      Doesn’t appear to be easily (user) extensible
        Limited insight into kernel / hardware state
        May be difficult to debug / repair

## Slide 34: Interfacing Android Things: Observations
What is “Embedded Programming”?
“Embedded programming” covers orders-of-magnitude spectrum
  Integrated solution (e.g., OS) unlikely to cover full spectrum
  Android Things applicable to only [very] upper end of spectrum
  We might need better terminology

## Slide 35: Interfacing Android Things: Observations
Java Thread and Asynchronous Events
I couldn’t make Java Thread class adequately handle asynchronous events
  Async link is full-duplex, peer-to-peer
    Thread must handle asynchronous events (receive character) plus timers

## Slide 36: Interfacing Android Things: Observations
Java Thread and Asynchronous Events
Android Thread extended with non-preemptive scheduler [sic]
  Looper
  Handler
Limited documentation / examples
  Documentation terse
  Some examples, advice appear possibly poor

## Slide 37: Interfacing Android Things: Observations
Java Thread and Asynchronous Events
It’s open source: Just look at the source code
  The code is the documentation

## Slide 38: Interfacing Android Things: Observations
“Just Look at the Source Code”
Handler
Looper
Message
Thread
Processes and Threads
Android Runtime
Dalvik bytecode

## Slide 39: Interfacing Android Things: Observations
Java String
This project passes ASCII strings between devices
  C handles strings pretty sort of well
    Single representation for char[] and string
      No conversion between representations

## Slide 40: Interfacing Android Things: Observations
Java String
This project passes ASCII strings between devices
  Java String objects are heavy weight in comparison
    Object creation is expensive
    String and byte[] representation are different objects
    No, I don’t care about character sets
    try/catch UnsupportedEncodingException???

## Slide 41: Interfacing Android Things: Observations
Hardware State Visibility
Project required visibility into state of hardware
  Android Things didn’t help at all
    Little access to state of hardware / kernel

## Slide 42: Interfacing Android Things: Observations
Hardware State Visibility
Project required visibility into state of hardware
  Most hardware debugging done on Arduino
    printf (although non-trivial)
    Display individual bytes received
    Display individual interrupts
    Displayed system state on three LEDs

## Slide 43: Interfacing Android Things: Observations
Hardware State Visibility
Project required visibility into state of hardware
  Needed to know low-level state of hardware
    Occasionally used VOM meter
    Yearned for oscilloscope

## Slide 44: Interfacing Android Things: Observations
Low-Level Development
Do embedded developers need to modify their own kernel or runtime code? Access to root?
  Is this consistent with Android Things approach?
  Is this scalable?
  I wonder about experience of production Android Things developers

## Slide 45: Interfacing Android Things: Observations
Mobile Developers Don’t
Fight with the hardware
  Celebrate the first successful bit transferred
  Yearn for an oscilloscope
  Think about noise / transmission lines / …
  Solder
  Prototype
    Breadboard / hunt for right jumper / …

## Slide 46: Interfacing Android Things: Observations
Mobile Developers Don’t
Examine each interrupt
  Count instructions in interrupt service routine
  Examine MCU register state
Think about memory
  Reduce buffer sizes to fit memory

## Slide 47: Interfacing Android Things: Observations
Mobile Developers Don’t
Want to know what lower-level state is
  Kernel
  Driver
  Hardware
Normally use Looper, Handler

## Slide 48: Interfacing Android Things: Observations
Mobile Developer

## Slide 49: Interfacing Android Things: Observations
Embedded Developer

## Slide 50: Interfacing Android Things: Observations
Whither Android Things?
Will Android Things become a useful tool for embedded programming?
  I would love to see Android Things become brilliantly successful
  But…

## Slide 51: Interfacing Android Things: Observations
Whither Android Things?
Will Android Things become a useful tool for embedded programming?
  Current focus on big iron
    Multi-core, GHz processors with half-a-gigabyte or more
  Seems unlikely to ever be useful for MCUs
  Useful on generic CPUs?
  Useful outside of Google ecosystem?

## Slide 52: Interfacing Android Things: Observations
Whither Android Things?
Will Android Things become a useful tool for embedded programming?
  Tied to Google ecosystem
  Focus appears to be on smart displays (large and small) and home automation hubs

## Slide 53: Interfacing Android Things: Observations
Whither Android Things?
Will Android Things become a useful tool for embedded programming?
  In my view, Google needs an edge computing solution
    Important for Google IoT Cloud

## Slide 54: Interfacing Android Things: Observations
Whither Android Things?
Will Android Things become a useful tool for embedded programming?
  Lots of competition in these spaces
  Even within Google
    Chrome
    Fuchsia
    Cloud IoT Edge / Linux

## Slide 55: Interfacing Android Things
Android Things “Makes embedded development as simple as mobile development has become”
  - Dave Smith, Google I/O 2017
  While the Android Things ecosystem demonstrates some potentially useful capabilities, it is no panacea for the challenges that face embedded developers.
  - Tim Salo, IoT Devfest 2019